## Slide 1: Status of MISR Stereo Motion Vectors and Assessment using MODIS, MSG, & CATS lidar
Kevin J. Mueller1
1Jet Propulsion Laboratory, California Institute of Technology, Pasadena, CA

## Slide 2: Multi-angle Imaging SpectroRadiometer
MISR Wind Products
Stereo Motion Vectors (SMV)
  Geometric height obtained from parallax
  Retrieved from redundant forward and aft camera triplets
  Time interval ∆t = 200 seconds
  Gridded resolution ∆x = 17.6 km
Height-resolved cross-track cloud motions:
  Geometric height obtained from parallax
  Retrieved from redundant forward and aft camera pairs
  Time interval ∆t = 46 seconds
  Gridded resolution ∆x = 1.1 km
MISR instrument
Mission Lifetime
  1999 -> 2018+ 2026
  Orbit change in 2022
Swath Width ~ 380 km
9 Camera View Angles
  0º (Nadir)
  ±26.1º, ± 45.6º
  ±60.0º, ± 70.5º
  7 minute overpass
B, G, R, & NIR Bands
Spatial Resolution
  275 m for Nadir and Red Band
  1100 m all else
Along-track
Cross-track
Up
∆t ~ 7 minutes
Along-track
Cross-track

## Slide 3: MISR Stereo Motion Vectors status
  Forecast benefit in GMAO GEOS-5 model shown
    Mueller et al. 2017, MWR
    GMAO following up by incorporating code into operational GEOS5-FP
      Testing in progress after updating code from paper to current GEOS5 revision
  Two years of NWPSAF monitoring show well constrained error
    NWPSAF AMV Analysis reports show 2 caveats:
      occasional orbits with poor georegistration have systematic bias and degraded forecast benefit
  MISR SMV will benefit from major upstream revisions to Level 1 software
    New DEM and revised camera model will benefit georegistration
    MISR SMV are highly sensitive to georegistration- see above

## Slide 4: Example MISR Wind Product Retrievals
Height resolved cross-track cloud motion (1.1 km resolution)
(Hurricane Ida)
Height resolved cloud motion vectors (17.6 km resolution)
(Hurricane Francis)
Height (meters)

## Slide 5: Research retrieval: 4.4 km resolution
Speed 20 m/s
Height (m)
9000
0
6000
3000

## Slide 6: Prototype: divergence @ 4.4 km
Divergence
(s-1 ×10-3)
0
-0.2
-0.4
0.2
0.4

## Slide 7: Questions from past SMV assessment
Comparison of MISR with GOES AMV (2003-2008)
  Mueller et al., 2017 JAMC
  MISR and GOES wind tracking agree well
    3.2 m s-1 VRMS (VIS channel)
    1.6 m s-1 RMS cross-track
  Except for…
    (2) Low heights (< 4 km):
      Heights uncorrelated
      MISR often 2 km below GOES
    (3) High heights (> 8 km)
      MISR often 1 km above GOES
Can analysis be corroborated / expanded with “truth” data for heights?
Notes: Spend time explaining (1), (2), and (3)

## Slide 8: MISR SMV height validation with CATS
10s of thousands of well distributed spatial coincidences within 5 minutes, 2015-2017
Latitude range 52° S. to 52° N
Coincidences with poor MISR orbit registration have been excluded
Locations and heights (m) of coincidences
Height distribution of collocations

## Slide 9: Lidar heights compare favorably with SMV heights
Directly comparable measurements yield low noise
  RMS 300 m
MODIS vs. CATS height
MODIS height (km)
MISR vs. GOES height
CATS height (km)
MISR height (km)
MISR vs. CATS height
CATS height (km)

## Slide 10: MISR stereo prefers optically thick, water clouds (possible bias in other clouds)
Ice and unkown phase clouds have double the height variance relative to CATS
  Liquid phase σ = 260 m, ice & unknown phase σ = 500 m
With decreasing optical depth, height “bias” relative to CATS increases from -250 m to -30 m
Would these patterns hold for along-track variance and bias?
MISR height minus CATS height (m)
Liquid phase, bias as function of tau (at 1064 nm)
Ice & indeterminate phase, bias
Ice & unknown phase, bias as function of tau
MISR height minus CATS height (m)
Frequency

## Slide 11: Additionally collocated MSG AMV shows SMV along-track bias may follows height bias
Pattern of SMV along-track bias vs. MSG AMV follows that of SMV vs. CATS height
  Positive/negative along-track bias at positive/negative fringes of height distribution which
For low clouds:
  height σ=600 m, along-track σ=3.5 m/s, cross-track σ=2.5 m/s
MISR Height (km)
CATS Height (km)
CATS Height (km)
CATS Height (km)
5
CATS Height
Frequency
MISR cross-track bias
MISR along-track bias
5
5
5
0
0
0
5
5
0
0
5
Wind Component (m/s)
-5
0
0

## Slide 12: Low optical depth ice clouds (cirrus?) produce along-track biased retrievals
The fringes of the prior distribution show the source of bias to be ice in prior distribution

## Slide 13: Conclusions and follow up work
Ice clouds are a source of positive along-track bias in MISR SMVs, and may be the dominant source
Can a scheme for flagging ice clouds be used to improve robustness of MISR SMVs