## Slide 1: WMO Gap Analysis 8th CGMS WGIII Risk Assessment Workshop

## Slide 2
Executive summary of the WP
WMO gap analysis for Earth observation and space weather observation capabilities against the requirements presented in WMO Vision for WIGOS 2040 was provided. It compares space-based observation capabilities recorded in OSCAR/Space to the WMO WIGOS Vision for 2040 requirements for the period of next decade. In this working paper detailed descriptions of the missing observations capabilities related to the specific observation types in WIGOS subcomponent 1 and 2 were given. The work summarises totally 16 gaps for Earth observation types and 5 gaps for space weather observation types as main concerns non-compliant with WIGOS Vision 2040 requirements. Out of these gaps many are including periodic totally missing observation capabilities. These are for Earth observations: UV/VIS/NIR sounder, precipitation and cloud radars, backscatter and dial lidars, IR/MW and SW occultation limb sounders and SW occultation lidar. Related to space weather it concludes gaps with regards to WIGOS subcomponents 1 and 2 in magnetograph, radiospectrograph, X-ray imager and spectrometer.

## Slide 3: WMO Gap Analysis of the space-based observation system capabilities
CGMS Baseline
WIGOS Vision 2040
User requirements
  CGMS Baseline (CGMS Risk Assessment)
    CGMS member and observers are committed to for at least the next decade;
  WMO User Requirements
    The needs expressed by the users reviewing the status of observing technologies (Rolling Requirements Review, RRR);
  The WIGOS Vision
    The projected developments of the WMO Integrated Global Observing Systems to meet long-term objectives of the RRR.
  The WMO Gap analysis compares the WIGOS Vision with existing and planned satellite programmes.

## Slide 4: OSCAR/Space gap analysis 2025
Compares the satellite information recorded in OSCAR/Space to the instrument capabilities in the WIGOS Vision 2040
The considered period is the 2026-2036 to support the CGMS WG III Risk Assessment based on space agency plans as in Dec 2025
The WMO Gap Analysis includes a wider range of satellites than the risk assessment e.g. those that are close to approval but not confirmed and some research missions. It does not include commercial missions.
The WMO Gap Analysis categorizes instruments according to the WIGOS satellite instruments.
Both Earth Observation and Space Weather gap analyses have been done
The complete gap analysis extends to 2050 to assist in new vision for 2050 (not presented here)

## Slide 5: Information sources used to update OSCAR/Space
Updates from space agencies via OSCAR/Space Support Team (O/SST) Members
  Only 7 out of 17 responded to the last update request
    CMA, GISTDA, JAXA, JMA, CSA, IMD, NSOAS
Presentations from the space agencies in the CGMS meetings
Gunter’s space page (monitored daily)
CEOS quarterly reports
Spaceflight Now/ Space News & other news sites
Live real time tracking of satellites for orbit information
Jonathan’s space report
NWP SAF monitoring
Bluesky messages

## Slide 6: Earth Observations for geostationary orbits

## Slide 7: Geostationary core constellation (Subcomponent 1)
Rows in pink = CGMS baseline instrument
Gap =

## Slide 8: Hyperspectral IR sounders on GEO
FY-4 series and MTG-S host hyperspectral IR sounders
Himawari-10 is planned to include a hyperspectral sounder from 2030
NOAA have plans with GEO-XO to cover the US from 2033
There are gaps over the West Atlantic, Indian and East Pacific oceans without confirmed plans in the next decade
CGMS baseline:
GEO – 3 slots: 79°-140°E range and 0°

## Slide 9: UV/VIS/NIR sounders on GEO
Sounding of the atmosphere using reflected solar radiation at UV and visible wavelengths is very limited at present
GEO-KOMPSAT-2B and TEMPO have such an instrument in orbit
MTG with Sentinel-4 enhances the coverage over Europe from 2026
This leaves gaps over America, W. Atlantic, Asia and the Pacific in the next decade, which is a significant gap in the planned observing system
CGMS Baseline:
GEO – 1 slots at 0°

## Slide 10: Earth Observations for polar orbits

## Slide 11: Sun-synchronous core constellation satellites in three orbital planes (morning, afternoon, early morning) and additional scatterometers on drifting orbit (Subcomponent 1)
Gap =
Rows in pink = CGMS baseline instrument

## Slide 12: Day-night visible imagery
Satellites with a day-night visible channel capability are only in the early morning (FY-3) and early afternoon (NOAA) orbits
There are no plans for day-night imagery in the late morning orbit
CGMS Baseline
LEO early morning and afternoon orbits

## Slide 13: Scatterometers
Only 2 orbits are projected to be covered from 2032 to 2035 with scatterometers
CGMS Baseline
LEO – 3 sun-synchronous orbits, early morning, mid-morning and afternoon orbits

## Slide 14: Microwave Imagers on LEO
Within the next few years the number of MW imagers are at risk to reduce with the retirement of the SSMIS instruments on the DMSP satellites
WSF-M1 is now in the early morning orbit (~05:00 LT) and could potentially replace SSMIS avoiding a gap followed by WSF-M2
CIMR will fill the 06:00 LT orbit in 2029
CGMS Baseline
LEO – 2 sun-synchronous orbits, nominally early morning, mid-morning, and afternoon

## Slide 15: Instruments on other satellites in low-Earth orbit (Subcomponent 1)
Gap =
Rows in pink = CGMS baseline instrument

## Slide 16: UV/VIS Nadir and Limb Sounders for atmospheric chemistry
For limb sounders (scanning or occultation views) the morning orbit in covered by OMS-Limb (FY-3F) out to 2032 and afternoon orbit by NOAA OMPS (up to 2041).
Typical requirements for stratospheric chemistry are for 6 hr sampling time so a 2 polar orbiter system should be maintained.
CGMS Baseline
LEO – 2 sun-synchronous orbits, mid-morning, afternoon
HLPP
1.2.1 Work towards establishing optimum constellations for new observations introduced in CGMS Baseline: UV limb sounding spectrometry for profiles of Ozone and trace gases.

## Slide 17: Low frequency microwave imager on LEO
Measuring the surface at the lower microwave frequencies (<10 GHz) is important for SST, soil moisture and salinity
The ESA proposal for CIMR (and Japanese AMSR-3 instruments) should ensure good coverage for the next decade, and HY-2 series provides coverage in the early morning orbit prior to CIMR.
Potential gap of < 5GHz after SMOS/SMAP retires before CIMR-A launched which impacts soil moisture/salinity.
Plans for long term continuity of these measurements should be put in place.
CGMS Baseline
Covered by general baseline for microwave imagers, no specific attributes for low-frequency instruments

## Slide 18: Precipitation radar and cloud radar on LEO
Precipitation radar:
  The GPM-DPR will provide coverage for this decade now as its end of life is extended
  FY-3 satellites (FY-3G/I) have a precipitation radar providing measurements into the next decade in a drifting orbit without redundancy.
Cloud radar:
  EarthCARE is the only cloud radar planned for this decade
  When EarthCARE retires there will be a gap until expected ESA WIVERN in mid 30’s. The user requirement for sampling is for 3 hourly or better.
CGMS Baseline
Precipitation radar: LEO – drifting orbit, nothing for cloud radar

## Slide 19: Total and spectral solar irradiance on LEO
Continuity of total solar irradiance measurements in polar orbits are planned by FY-3E/J
The spectral solar irradiance observations will be reduced after 2028 when ISS-TSIS-2 is retired, and after that FY-3E/F/J will provide continuity in the early morning orbit.
CGMS Baseline:
Not included

## Slide 20: Backbone system with open orbit configuration and flexibility to optimize the implementation (Subcomponent 2)

## Slide 21: Doppler Wind Lidar and backscatter lidar on LEO/Drift
After the retirement of Aeolus there is now a gap in coverage until the planned launch of EPS-Aeolus in 2034
Doppler wind lidars should be considered on a more operational basis as the technology improves
Backscatter and DIAL lidar relies on EarthCARE/MERLIN and DQ-1/2. No plans for longer term.
Altimeter lidar capability also not clear in next decade.
CGMS Baseline
Not specified at present
HLPP
1.2.7 Work towards operational 3D wind profile observations from space-based lidar

## Slide 22: Limb sounder in IR and MW on LEO/Drift
After Aura/MLS and Odin are retired shortly, no limb sounders will be operating in the IR and MW
At present there are no planned successors to MLS leading to a loss of valuable information on stratospheric chemistry and a discontinuity in any climate data records from these measurements
CGMS Baseline
Not specified
HLPP
1.2.8 Work towards operational infrared/µwave limb sounding for climate monitoring and NWP applications

## Slide 23: Greenhouse gas measurements
To monitor greenhouse gases Microcarb and CO2M will provide continuity of measurements for UV/VIS/NIR spectrum at high spectral resolution through this decade and most of next decade.
Many small research satellites will provide observations in short term.
There is a strong requirement to continue these measurements to monitor greenhouse gas concentrations, but there are no firm plans for operational long-term monitoring beyond 2035 in 2 orbits
Only planned long-term mission is Sentinel-5 on Metop-SG but it does not monitor CO2
CGMS Baseline
SWIR imaging spectrometer in 2 sun-synchronous orbits late morning and afternoon
Instrument | Satellite
CO2I and NO2I | CO2M
IASI-NG | Metop-SG-A1
Sentinel-5 | Metop-SG-A1
IASI | Metop-B
IASI | Metop-C
MicroCarb | MicroCarb
Carbon Mapper | Tanager-1
Carbon Mapper | Tanager-2
TANSO-3 | GOSAT-GW
GMI (GF-5) | GF-5-02
GMI (GF-5) | GF-5-01A
OCO | OCO-2
GAS-2 | FY-3H
OCO (ISS) | ISS OCO-3
GHGSat-Spectrometer | GHGSat
ACDL | DQ-1
ACDL | DQ-2
GHG measurements 2026:

## Slide 24: High Temporal MW Sounders on LEO/Drift
NOAA-15/18/19 MW sounders and TROPICS are retired, so the operational MW sounders are now only in 3 orbits.
The approved EPS-Sterna programme will mitigate this with several complimentary orbits
Future commercial satellite constellations in orbit (Tomorrow-IO-S1-S11) and others in planning may also contribute
Potential decrease in MW sounder coverage in short term.
CGMS Baseline:
3 sun-synchronous orbits, nominally early morning, mid-morning and afternoon
HLPP:
1.2.5 Establish observational requirements for microwave observations (sounder and imager) for NWP and precipitation and perform gap analysis against CGMS baseline;

## Slide 25: GNSS Reflectometry on LEO/Drift
The coverage of the GNSS reflectometry capability degrades into the next decade with only the FY-3 satellites providing it
Currently there are research missions and some private sector plans to demonstrate the benefits of this type of measurement
CGMS Baseline
Soil moisture is mentioned, but not specifically GNSS reflectometry sensor type.

## Slide 26: SW occultation limb sounding
Altius providing current observations but EoL is 2030. No plans for next decade.
CGMS Baseline
Not specified

## Slide 27: MW sounding on GEO
Only the CMA FY-4 GEO satellite is planning to fly a prototype instrument in the near future.
CGMS Baseline
Not specified

## Slide 28: The most critical EO gaps for the next 10 years
UV/VIS/NIR Sounders on GEO
Doppler Wind Lidar on LEO/Drift
Only 2 orbits covered with scatterometer from 2032-2035
Backscatter and DIAL lidars have no firm plans for next decade
Limb sounders in IR and MW on LEO/Drift
Reducing precipitation radar coverage and gap in cloud radar
No SW occultation lidars in next decade

## Slide 29
Gaps against WIGOS Vision for Earth Observation

## Slide 30: Space weather

## Slide 31
Solar Remote Sensing Observations
Rows in pink are part of CGMS baseline
and can be linked to a specific orbit

## Slide 32: Gaps against WIGOS Vision
Interplanetary solar wind and magnetic field
Rows in pink are part of CGMS baseline
Magnetosphere
Ionosphere and Thermosphere

## Slide 33: Solar EUV spectrometers and imagers
For the Sun-Earth line once IMAP retires around 2029 there will be no EUV spectrometer or imager measurements from L1 but many from GEO/LEO orbits
The Solar Orbiter platform has an EUV spectrometer out to the end of this decade
ESA Vigil-L5 mission will provide EUV imagery from 2031-2038 for off-Sun-Earth line
A mission to continue EUV measurements at L1 for the next decade could be considered but not in current baseline
CGMS Baseline
GEO 2 slots
LEO 1 orbit

## Slide 34: Interplanetary solar wind and magnetic field observations from L1 and L5 orbits (L1/L5)
Measurements of the solar wind (including magnetic field) from L1 will rely on ACE, SWFO-L1, DSCOVR and IMAP to cover to the end of this decade
Only SWNext-L1A/B planned for next decade after which there are no approved missions to L1
Vigil will cover the L5 position for magnetic field into the next decade but these measurements don’t replace those from L1.
CGMS Baseline:
Plasma Analyser + particle sensor + magnetometer in L1 as in-situ measurement

## Slide 35: Solar coronagraphs
For solar coronagraph observations at L1 SWFO-L1 and SWNext-SOL-A/B planned
Several other coronagraph observations from GEO/LEO orbits
Vigil will provide coronographic imagery at L5 from 2031
Plans are needed for long term continuity from L1 and L5
CGMS Baseline:
Sun-Earth line (From GEO 1 slot and L1)

## Slide 36: In-situ observations in Magnetosphere
The space particle environment is measured in all 6 baseline geostationary orbits out to 2033
The Russian LEO Ionosfera satellites can contribute to space particle measurements lower down up to 2032 and the Arctica satellites are in Molnya orbits.
The geomagnetic field is nominally measured in 5 geostationary orbits out to 2035 but from only 1 LEO orbit (FY-3) in the Ionosphere by the mid 30’s
CGMS Baseline:
4 GEO slots for magnetometer
2-3 GEO slots for in-situ particles

## Slide 37: Summary chart of Space Weather observations in 2032-2036

## Slide 38: Space Weather gaps to consider for the next 10 years
Only 1 coronograph in GEO orbit from 2031 and only 1 at L1
Only 1 satellite measuring solar wind and magnetic field at L1 from 2034
No solar magnetograph at L1 from 2029
No radio waves measured at L1 from 2031
No EUV spectrometer or imager measurements at L1 from 2030

## Slide 39: Questions?