## Slide 1: NASA Response to Open Actions from 7th Risk Assessment Workshop Presented to 8th Risk Assessment Workshop Eric McVay, Program Executive Earth Science Division, NASA Headquarters

## Slide 2
3.1 Continuity of GPM
Ref. 7RAWS-4: NASA and JAXA to provide a coordinated additional information on possible GPM continuation mission
GPM performed two orbit boost maneuvers in November 2023 to raise its altitude and restore its lifespan closer to the original estimates of ending in the early 2030s. NASA is working with JAXA to maintain continuity of this important precipitation measurement.

## Slide 3
3.2 IMAP and CGMS baseline
Ref. 7RAWS-5: NASA on IMAP mission and if its data is compliant with CGMS baseline criteria
IMAP: The latency requirement is <5 minutes for data that is received on the ground and then processed and delivered to the space weather community. The space weather data set only includes the data from the five space weather relevant instruments and the necessary spacecraft ancillary data to make it useful. Those instruments include CoDICE (Compact Dual Ion Composition Experiment), HIT (High-energy Ion Telescope), SWAPI (Solar Wind and Pickup Ion), SWE (Solar Wind Electron), and MAG (Magnetometer).
  I-ALiRT is dependent on the establishment of a global ground station network. We currently have agreements with South Korea and Germany. We continue to work on agreements with partners in the southern hemisphere and South America.
Post-Workshop update: there is not a requirement or timeline for when the global network will be complete such that we have no I-ALiRT gaps. The network is built upon no-exchange of funds partnerships, which takes some coalition building to get it done. We’ve seen a lot more enthusiasm from potential partners since launch and hope to dovetail that interest into agreements. Recommend not including this in the baseline until the network is fully developed/in place.

## Slide 4
3.3 L5 JEDI and CGMS baseline
Ref. 7RAWS-10: NASA and ESA to confirm if the L5 JEDI mission and its data is compliant with CGMS Baseline criteria
JEDI: NASA is contributing the JEDI instrument to ESA’s Vigil mission, which will produce data for both a low latency operational channel and the higher latency science data channel. For Vigil operational data, they have a <5min latency 24/7 requirement for the operational data that will go through ground stations to the forecasting offices. NOAA will be responsible for the official processing of CCOR-3 data and for distributing to their partners and customers.
  If ESA has clarifying information about Vigil – as the mission lead – we would defer to that.
Post-Workshop update: JEDI is assessed to meet the key principles for inclusion in the CGMS Baseline and supports the EUV Imager solar/space observation line.